|  | ......................... Pcs. .............................. € .............................. € GEZE GCER 300, 1-door SET Access control solution with RFID reader and PIN keyboard in stand-alone operation for controlling one door (can be extended to 2 doors). RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). An ID card can be assigned one of two types of authorisation for the short-term release or permanent release (office function) of doors and gates. Door release time can be selected from 1-99 seconds. The length of the PIN can vary between 4 and 6 characters. Communication between reader and control unit takes place by encrypted data transfer. Functions such as interlocking door system or dementia can be set using DIP switches. Release buttons can be connected. Set consisting of: 1x GEZE GCER 300 I/O box Controls the opening process for 1 door (max. 2 possible) for installation in the secured area Control unit pre-mounted in PVC housing for surface mounting. Number of persons to be managed: max. 200 Voltage supply: 8 to 30 V DC Power consumption: max. 1.5 VA Service temperature: -20 °C to +60 °C Outputs: 4 relays (changers), 2 relays per door Contact load: max. 30 V DC, 1 A Inputs: 4 inputs, 2 per door Interface: 2x RS485 (2-wire), not galvanically isolated Type of connection: Screw/plug-in terminals IP rating: IP30 in housing (acc. to EN 60529) Dimensions (W x H x D): 150 x 100 x 36 mm (ID no. 185707) 1x GEZE GCVR 300 T, RFID reader UP With keypad (12 keys) For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Voltage supply: 8 to 30 V DC (internal reverse polarity protection) Power consumption: max. 1.7 VA Service temperature -25 °C to +60 °C Interface: 1x RS485 (2-wire) Type of connection: Clip connector pluggable IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 81 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 81 x 40 mm (surface mounted) (ID no. 185708) Optional 1x GEZE GCVR Touch 300 T, RFID reader UP With capacitive keyboard (12 keys) Classy glass look For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Voltage supply: 8 to 30 V DC (internal reverse polarity protection) Power consumption: max. 3.5 VA Service temperature -25 °C to +60 °C Interface: 1x RS485 (2-wire) Type of connection: plug-in 8-pole screw/plug-in terminal IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 101 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 101 x 41 mm (surface mounted) (ID no. 187108) 2x GEZE GCER 300 Master system card As a security card for system administration GEZE logo and Master printed on the front Colour: white on both sides (ID no. 185713) 10x GEZE RFID ID card RFID identification medium with print GEZE logo and serial number printed on the front Colour: white on both sides (ID no. 185711) Optional 10x GEZE RFID key fob RFID identification medium with print Serial number printed on the front GEZE logo on the back Round shape Colour: black, white cover (ID no. 185712) |
| --- | --- |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCER 300, 2-door SET Access control solution with RFID reader and PIN keyboard in stand-alone operation for controlling one door (can be extended to 2 doors). RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). An ID card can be assigned one of two types of authorisation for the short-term release or permanent release (office function) of doors and gates. Door release time can be selected from 1-99 seconds. The length of the PIN can vary between 4 and 6 characters. Communication between reader and control unit takes place by encrypted data transfer. Functions such as interlock or dementia can be set using DIP switches. Release button lockable. Set consisting of: 2x GEZE GCER 300 I/O box Controls the opening process for 1 door (max. 2 possible) for installation in the secured area Control unit pre-mounted in PVC housing for surface mounting. Number of persons to be managed: max. 200 Voltage supply: 8 to 30 V DC Power consumption: max. 1.5 VA Service temperature: -20 °C to +60 °C Outputs: 4 relays (changers), 2 relays per door Contact load: max. 30 V DC, 1A Inputs: 4 inputs, 2 per door Interface: 2x RS485 (2-wire), not galvanically isolated IP rating: IP30 in housing (acc. to EN 60529) Dimensions (WxHxD): 150 x 100 x 36 mm (ID no. 185707) 2x GEZE GCVR 300 T, RFID reader UP With keypad (12 keys) For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Voltage supply: 8 to 30V DC (internal reverse polarity protection) Power consumption: max. 1.7 VA Service temperature -25 °C to +60 °C Interface: 1x RS485 (2-wire) Type of connection: Clip connector pluggable IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 81 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 81 x 40 mm (surface mounted) (ID no. 185708) Optional 2x GEZE GCVR Touch 300 T, RFID reader UP With capacitive keyboard (12 keys) Classy glass look For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Voltage supply: 8 to 30V DC (internal reverse polarity protection) Power consumption: max. 3.5 VA Service temperature -25 °C to +60 °C Interface: 1x RS485 (2-wire) Type of connection: plug-in 8-pole screw/plug-in terminal IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 101 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 101 x 41 mm (surface mounted) (ID no. 187108) 2x GEZE GCER 300 Master system card As a security card for system administration GEZE logo and Master printed on the front Colour: white on both sides (ID no. 185713) 10x GEZE RFID ID card RFID identification medium with print GEZE logo and serial number printed on the front Colour: white on both sides (ID no. 185711) Optional 10x GEZE RFID key fob RFID identification medium with print Serial number printed on the front GEZE logo on the back Round shape Colour: black, white cover (ID no. 185712) |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCER 300 Light, 1-door SET Access control solution with RFID reader and PIN keyboard in stand-alone operation with a relay output for controlling one door located in the secured interior area. RFID frequency 13.56 MHz. Authorisation is granted through master ID cards in combination with PIN keyboard directly at the reader. Up to 200 persons/ID cards can be authorised for short-term release of doors and gates. If individual ID cards are lost or become faulty, they can simply be deleted from the system (selective deletion). Door release time can be selected from 1-99 seconds. The length of the PIN can vary between 4 and 6 characters. Communication takes place via encrypted data transfer. Set consisting of: 1x GEZE GCER 300 Light, RFID reader UP With keypad (12 keys) For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Number of persons to be managed: max. 200 Voltage supply: 8 to 30V DC (internal reverse polarity protection) Power consumption: max. 2.5 VA Service temperature -20 °C to +60 °C Type of connection: Clip connector pluggable Outputs: 1x relay contact Switching voltage: 30 V/DC Switching current: 1 A/DC IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 81 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 81 x 40 mm (surface mounted) (ID no. 185710) 2x GEZE GCER 300 Master system card As a security card for system administration GEZE logo and Master printed on the front Colour: white on both sides (ID no. 185713) 10x GEZE RFID ID card RFID identification medium with print GEZE logo and serial number printed on the front Colour: white on both sides (ID no. 185711) Optional 10x GEZE RFID key fob RFID identification medium with print Serial number printed on the front GEZE logo on the back Round shape Colour: black, white cover (ID no. 185712) |
|  | Individual components: |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCER 300 I/O box Controls the opening process for 1 door (max. 2 possible) for installation in the secured area Control unit pre-mounted in PVC housing for surface mounting Number of persons to be managed: max. 200 Voltage supply: 8 to 30 V DC Power consumption: max. 1.5 VA Service temperature: -20 °C to +60 °C Outputs: 4 relays (changers), 2 relays per door Contact load: max. 30 V DC, 1A Inputs: 4 inputs, 2 per door Interface: 2x RS485 (2-wire), not galvanically isolated IP rating: IP30 in housing (acc. to EN 60529) Dimensions (WxHxD): 150 x 100 x 36 mm (ID no. 185707) |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCVR 300 T, RFID reader UP With keypad (12 keys) For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Voltage supply: 8 to 30V DC (internal reverse polarity protection) Power consumption: max. 1.7 VA Service temperature -25 °C to +60 °C Interface: 1x RS485 (2-wire) Type of connection: Clip connector pluggable IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 81 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 81 x 40 mm (surface mounted) (ID no. 185708) |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCVR Touch 300 T, RFID reader UP With capacitive keyboard (12 keys) Classy glass look For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Voltage supply: 8 to 30V DC (internal reverse polarity protection) Power consumption: max. 3.5 VA Service temperature -25 °C to +60 °C Interface: 1x RS485 (2-wire) Type of connection: plug-in 8-pole screw/plug-in terminal IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 101 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 101 x 41 mm (surface mounted) (ID no. 187108) |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCER 300 Light, RFID reader UP With keypad (12 keys) For installation in flush-mounted box 60 mm or for surface mounting in conjunction with surface-mounting frame (optional) Optical signalling through 3 LEDs (red, green, orange) Acoustic signalling via integrated buzzer Frequency: 13.56 MHz, ISO 14443 A Number of persons to be managed: max. 200 Voltage supply: 8 to 30V DC (internal reverse polarity protection) Power consumption: max. 2.5 VA Service temperature -20 °C to +60 °C Type of connection: Clip connector pluggable Outputs: 1x relay contact Switching voltage: 30 V/DC Switching current: 1 A/DC IP rating: at the front (in mounted state) IP54 Dimensions (W x H x D): 81 x 81 x 21 mm (flush mounted) Optional dimensions (W x H x D): 81 x 81 x 40 mm (surface mounted) (ID no. 185710) |
|  | ......................... Pcs. .............................. € .............................. € GEZE GCER 300 Master system card As a security card for system administration GEZE logo and Master printed on the front Colour: white on both sides (ID no. 185713) |
|  | ......................... Pcs. .............................. € .............................. € GEZE RFID ID card RFID identification medium with print GEZE logo and serial number printed on the front Colour: white on both sides (ID no. 185711) |
|  | ......................... Pcs. .............................. € .............................. € GEZE RFID key fob (optional) RFID identification medium with print Serial number printed on the front GEZE logo on the back Round shape Colour: black, white cover (ID no. 185712) |
|  | ......................... Pcs. .............................. € .............................. € GEZE surface-mounted frame GCER AP (optional) PVC housing for surface mounting of the readers GCVR 300 Dimensions (W x H x D): 81 x 81 x 30 mm Overall depth with reader 40 mm (ID no. 130024) |
|  | ......................... Pcs. .............................. € .............................. € Plug-in power supply NT 1.0 A – 24 V DC (optional) Primary: 230 V AC, 50 Hz Secondary: 24 V DC (+/- 5 %) / 1 A (ID no. 130025) |
|  | ......................... Pcs. .............................. € .............................. € Power supply NT 1.1 A– 24 V DC UP (optional) For installation in deep standard flush-mounted boxes Primary: 230 V AC, 50 Hz Secondary: 24 V DC / 1.1 A (ID no. 151426) |
|  | ......................... Pcs. .............................. € .............................. € Power supply NT 1.5 A – 24 V DC HA (optional) For installation on top hat rails Primary: 230 V AC, 50 Hz Secondary: 21.6 – 26.4 V DC / 1.5 A (ID no. 151426) |