|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer system TS 4000 E-IS 24 V DC, for double leaf doors, for installation on fire and smoke protection doors, with electrical hold-open device with variable adjustment from 80° to 175° in accordance with EN 1155, with integrated closing sequence control, with infinitely adjustable closing force size 1 – 6 in accordance with EN 1154; closing force and closing speed are front adjustable, with visual closing force display, standard installation on door leaf/hinge side, with mounting plate Colour: ( ) silver-coloured ( ) acc. to RAL Note: The GEZE TS 4000 E-IS has been approved and certified for use with various trigger mechanisms. Please note the general building approval from DIBt (German institute for construction technology). |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE RSZ 7 smoke switch control unit, suitable for installation on fire and smoke protection closers, extendable, with telescopic function, for bridging unfavourable lintel situations, 30 mm overall height, in GEZE design, with adaption of the alarm threshold, contamination indicator and integrated test button, integrated line monitoring to ceiling-mounted detector and manual trigger switch, for connection of GEZE hold-open devices, approved by DIBt as hold-open system for fire protection closers, EN 14637 compliant Connection: 230V AC Output voltage: 24 V DC, 250 mA For lintel height > 1 m, 2 additional ceiling-mounted detectors are needed. Colour: ( ) silver-coloured ( ) white ( ) stainless steel effect ( ) RAL ….. |
|  | ......................... Pcs. .............................. € .............................. € GEZE FA GC 170 wireless extension for connecting wireless components to GEZE hold-open systems without cables, consisting of: GEZE GC 171 wireless module for connection to GEZE hold-open systems, 24 VDC supply directly via GEZE hold-open system, set up with dip switch without additional programming tools, display of connection quality and status for every device, encrypted wireless connection, wireless integration of up to six devices GC 172 / GC 173 / GC 175 tested in accordance with EN 54-25 and EN 54-18, general type approval for GEZE hold-open systems ( ) GEZE GC 172 wireless ceiling-mounted smoke detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-7 and EN 54-25, with adaption of the alarm threshold in accordance with DIN14677, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 173 wireless ceiling-mounted thermal detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-5 and EN 54-25, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 175 wireless input module for wireless connection to the GEZE GC 171 wireless module, connection to manual trigger switch or potential-free contact of a fire alarm system, encrypted wireless connection, battery operated, battery life 5 years, tested in accordance with EN 54-25 and EN 54-18, installed in flush mounted socket EN 14637 compliant, general type approval for GEZE hold-open systems |
|  | ......................... pcs. .............................. € .............................. € GEZE smoke detector GC 152, 24 V, complete with base, tested in accordance with EN 54-7, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE thermal detector GC 153, 24 V, complete with base, tested in accordance with EN 54-5, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |
|  | ......................... pcs. .............................. € .............................. € Acceptance test for the hold-open system and permanent attachment of the sign of approval |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (standard) Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (optional position) with warranty extension Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months at the latest after the commissioning date) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - No separate charging for consumables up to EUR 25 per maintenance service - No separate charging for working hours when spare parts are replaced during the maintenance - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without additional costs (exceptions: Sundays and national holidays) - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |