|  | ......................... pcs. .............................. € .............................. € GEZE Slimdrive SL NT Compact automatic linear sliding door with only 70 mm drive height, type-tested by the German Association for Technical Inspection according to DIN 18650 / EN 16005, for leaf weights up to 125 kg per leaf, with self-cleaning rollers for permanently smooth running Drive Drive dimensions H x D: 70 x 190 mm Integrated battery with automatic charge and monitoring functions for opening or closing in the event of a power failure Intelligent digital control (Category 2 in accordance with DIN EN 954-1 and Performance Level “d” in accordance with DIN EN ISO 13849-1): - Convenient parameter setting, commissioning and maintenance via optional Bluetooth connection to a PC - Self-learning and with dynamic adaptation of the passage hold-open time for optimum convenience - Can be networked and integrated in building systems via CAN-bus - Independent fault detection and protocol - Adjustment options for all door movement parameters - All functions integrated in one unit, no further modules necessary Extremely quiet running direct current drive Robust power supply with integrated all-pole main switch and fuse protection Static and dynamic power limitation according to DIN 18650 / EN 16005, as well as static under 150 N in accordance with ASR A1.7 (formerly BGR 232) Automatic reversal when obstacles are detected Construction dimensions (dimensions in unfinished state): Clear overall height LH:............... mm Clear construction width LB:............... mm Passage height DH:.............. mm Passage clearance DB:............. mm (1-leaf 900* - 3000 mm) *900 mm on account of DIN 18040 Type of installation: ( ) Wall installation or ( ) Installation on profile system or ( ) Cantilever installation Door system version: ( ) Single-leaf closing on the left ( ) Single-leaf closing on the right ( ) With side parts Fitting: ( ) On-site moving leaf Surface of the light alloy parts of the drive and the moving leaves if appropriate: ( ) Anodised EV1 or ( ) RAL ........ Wiring to be carried out on site according to the GEZE cable plan by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in compliance with DIN 18650 / EN 16005 through plant fitters or service partner. In compliance with DIN 18650 / EN 16005: - Safety analysis must be carried out as a basis for planning and execution - An inspection must be carried out at least 1 x year and maintenance at least 1 x year. If there is no protection, the safety analysis must refer to the residual risk. Activation devices: Outside: 1 switch for opening the door (see 1.4) 1 indicator lamp (red) for visual “OCCUPIED” display, 24 V AC, white 1 emergency opening switch in a lockable box with glass pane (see 1.7) Inside: 1 switch for opening and closing the door (see 1.4) 1 indicator lamp (red) for visual “OCCUPIED” display, 24 V AC, white |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Operation GEZE display programme switch in the AS 500 range for setting the mode of operation as well as for commissioning and setting the parameters of the drive, with control keys, 2x 7-segment display, alphanumerical fault display, IP rating IP 40 Operating modes: permanently open, automatic, shop closing, night-locking, off ( ) Surface-mounted ( ) Flush-mounted or GEZE keypad programme switch for setting the mode of operation, with control keys, LED dot display, coded error display, IP rating IP 40, suitable for switch product ranges with 55 x 55 mm switch unit Operating modes: off, permanently open, automatic, shop closing, night-locking ( ) Surface-mounted ( ) Flush-mounted or GEZE mechanical programme switch for setting the mode of operation, with key, LED fault display, IP rating IP 40, suitable for switch programmes with 55 x 55 mm switch unit Operating modes: off, permanently open, automatic, shop closing, night-locking ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Operation (optional position) GEZE key switch to “lock” the programme switch to prevent unauthorised changing of the mode of operation, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted ( ) Euro profile half cylinder |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 339+ active infrared detector with two light curtains for protecting the opening or closing area in accordance with DIN 18650 / EN 16005, IP54 rating, 10 possible light curtain configurations Version: ( ) black ( ) according to RAL ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling ( ) Smart Daisy Chain Hub for series connection of up to three sliding door sensors |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GC 341 active infrared detector with two light curtains for protecting the opening or closing area according to DIN 18650/EN 16005, IP54 rating, 4 possible light curtain configurations Version: ( ) black ( ) interior ( ) exterior Accessories: ( ) outside: weather hood to protect the sensor from the interference of rain ( ) Ceiling installation bracket ( ) Ceiling installation kit for integrating the active infrared detector in the ceiling |
|  | ......................... pcs. .............................. € .............................. € Activation (optional position) GEZE elbow switch, plastic, IP rating IP 30 Dimensions: 90 x 180 x 23 mm ( ) White ( ) Stainless steel ( ) Surface-mounted or GEZE elbow switch, LS990, IP rating IP 30 Dimensions: 81 x 223 x 51 mm ( ) White ( ) Stainless steel ( ) Surface-mounted ( ) Flush-mounted or GEZE elbow switch, stainless steel, IP rating IP 65 Dimensions: 72 x 250 x 17 mm ( ) Surface-mounted or GEZE non-contact proximity switch (radar) Plastic with antimicrobial surface, IP rating IP65, multi-colour LED feedback, adjustable acoustic feedback. Additional input to actively change the LED colour. Dimensions: 80 x 80 mm ( ) Flush mounting 12 mm deep ( ) Surface mounting 21 mm deep ( ) Variant for WC or GEZE LED sensor push button, plastic, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor push button, glass, IP rating IP 69K round, diameter: 100 mm ( ) Flush-mounted ( ) Surface-mounted: mounting ring flat 4 mm ( ) Surface-mounted: mounting ring high 20 mm or GEZE LED sensor foot switch, glass, IP rating IP69K Dimensions: 100 x 100 x 3 mm ( ) flush-mounting ( ) vertically adjustable installation base for depths of up to 215 mm from the unfinished floor or External lamp red, AS 500 Plastic, alpine white IP rating IP20 Dimensions flush mounting (WxHxD) 81x81x41mm ( ) internal ( ) external ( ) surface-mounted ( ) flush-mounted or Signal horn, AS 500 Plastic, alpine white for acoustic signalling Dimensions flush mounting (WxHxD) 81x81x41mm ( ) surface-mounted ( ) flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE protective leaf for protecting against shearing, nipping and trapping positions according to DIN 18650 / EN 16005 in front of the moving leaf, leaves made of 10 mm ESG (toughened safety glass) including fitting, can be turned for cleaning purposes May only be used together with fine-framed moving leaf with ISO-glass or with integrated IGG fitting. ( ) Fastening on the drive or ( ) Fastening on the wall alternatively: ( ) Sensor-controlled side panel protection using 3D light curtain |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE safety leaf for protecting against shearing and nipping positions in accordance with DIN 18650 / EN 16005 with post-rail structures (depending on the offset between post surface and facade glazing) behind the moving leaf, leaf made of 10 mm ESG (toughened safety glass) incl. fitting alternatively: ( ) Sensor-controlled side panel protection using 3D light curtain |
|  | ......................... pcs. .............................. € .............................. € Protection (optional position) GEZE emergency stop switch with glass pane and lighting for switching off the mains voltage, IP rating IP 20 An emergency command device (emergency stop switch) is not essential for compliance with DIN 18650 / EN 16005. ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Locking (optional position) ( ) Two-stage electromagnetic locking, integrated in the drive, with manual emergency unlocking |
|  | ......................... pcs. .............................. € .............................. € Floor guide (optional position) Continuous floor guide made of anodised aluminium E6/EV1, can be installed flush in the floor, guide rail can be removed for cleaning or replaced Recommended for external doors with opening widths greater than 2000 mm |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing (option) Service package for maintenance and inspection in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years e.g. GEZE compact service package |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance in accordance with EN 16005, DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to EUR 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - exclusive package Service maintenance (optional position) Exclusive service package for servicing, maintenance in accordance with DIN 18650 Part 2 and ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 60 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Complete repair: no separate charging for repairs (parts and working hours) and travel costs during the contract run time - Online access for the client to the project and system data at the contractor’s - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 5 years |